Videoconferencing Continuum

Desktop VC: Skype, iChat, etc.

- Free

- Proprietary (i.e. Skype only connects to Skype, iChat only connects to iChat, etc).

- Disadvantage: No echo-cancellation can make it difficult to use with a full classroom.

- No (or limited) multipoint capabilities.

- Inability to use peripherals for additional visuals.

Desktop VC: Open Source H.323

H323 is the standard for what is also referred to as IP based videoconferencing. With H323 you can connect to any other H323 device.

- Free

- Ekiga and XMeeting

- Connects to most H323 standard videoconferencing units

- Disadvantage: No echo-cancellation can make it difficult to use with a classroom of students

Desktop VC: H.323

- Polycom PVX software: $120 ish plus webcam

- Polycom CMA: desktop software that requires a server

- Tandberg Movi: desktop software that requires a server

- Echo-cancellation may be a problem

- Rigging audio and video from a desktop system to work in a classroom can be challenging

Small Room Systems: Fixed Camera H.323

- Under $5000

- Polycom V500, VSX 5000

- LifeSize Express w/Focus camera

- Cameras have limited or no movement

- Designed for small conference rooms, 3-7 people

- Easy to receive content from content providers etc., but difficult to use to have students present for events like Read Around the Planet and other collaborative projects

Classroom Systems: H.323 SD (standard definition)

- Range from $3000-$9000 (ask your vendor for an “entry level” unit)

- The older units are “set top” units that were designed to sit on a TV; newer units separate camera & codec to accommodate flat screen monitors

- Ability to connect a computer and document camera for presenting

- Great camera movement, ideal for classrooms

- Polycom VSX 7000  and 8000 series (older)

- Polycom QDX (newer, faster, better, cheaper)

- Tandberg 770, 880, 990 MXPs (older)

Classroom Systems: H.323 HD (high definition)

- To take full advantage of HD, calls need to be at 1-4 M. Most schools don’t have that bandwidth available; most content providers still make calls at 384K. Still, these systems have better cameras.

- It’s an investment in the future of the technology.

- Lifesize Express, Express 200, Team MP, Team 200, Room, and Room 200

- Polycom HDX 7000, 8000 9000 series

- Tandberg QuickSet C20 (newer, entry level HD unit)

- Tandberg Edge MXPs 75, 85, 95

For more information on carts vs. rooms and videoconferencing network infrastructure, read the full article this text was extracted from: http://vcoutonalim.org/2009/08/04/continuum-of-videoconferencing/